## Slide 1
HEV Supervisory Control and Fault Diagnosis
Module 3 Introduction

## Slide 2
Module 3
Engine and Generator Control
HEV Supervisory Control and Fault Diagnosis

## Slide 3: Module Overview
Controlling the engine and generator is key function of the supervisory control:
  Dictates what operating mode
  Dictates the torque and speed operation of the engine and generator
  Review thermostatic control is the most basic control that could be applied to operate the engine and generator
Design of the supervisory control requires optimization
  What operating points give best efficiency while meeting power demand?

## Slide 4: Module Overview
In this module, we will do the following:
  Review how the engine, generator, and battery operate together
  Review charge depleting and charge sustaining mode
  Examine how the supervisory control uses torque control to control the engine
  Examine how the supervisory control uses speed control to control the generator
  Discuss how thermostatic control can be used to operate the engine and generator
  Demonstrate how to optimize engine and generator operating points to achieve a minimum power request

## Slide 5
AVTC Model Based Design Curriculum Development Project

## Slide 6
HEV Supervisory Control and Fault Diagnosis
Module 3-1

## Slide 7: Review of engine/generator operation
Lesson 3-1
Module 3
Engine and Generator Control

## Slide 8: Introduction
Review of basics of a series HEV
Role of a Supervisory Control
Role of Sub-Controllers
Possible Control Modes for Series Operation

## Slide 9: Engine/Generator Block Diagram
All components electrically parallel
Generator attached to engine

## Slide 10: Governing Equations
Where:

## Slide 11: Modes of Operation
Two modes of operation
  Charge Sustaining
    Keep SOC (state of charge) within certain threshold
      Engine on
    Maximize efficiency while meeting driver torque request
  Charge Depleting
    Electric motor only (Engine off)
      Depletes SOC
    Can also have blended mode
      Not covered in this module

## Slide 12: Modes of Operation
Blended Mode
EREV (Extended Range Electric Vehicle) Mode

## Slide 13: Modes of Operation
Charge sustaining
  All components in use

## Slide 14: Modes of Operation
Charge Depleting
  Option 1: All-Electric Mode (no engine usage)
  Option 2: Blended Mode (some engine usage)

## Slide 15: Generator/Engine Operation
Supervisory controls generally issue reference requests to lower-level controls
  The Supervisory Control is the “brains” of the operation and doesn’t get involved in the details
  The other controls follow orders and worry about achieving the reference request
For an Series HEV, a Supervisory control could request engine torque and generator speed:
  Requests go to low-level controllers
    Engine torque - ECU
    Generator speed - Inverter

## Slide 16: Generator/Engine Operation

## Slide 17: Torque Control

## Slide 18: Torque (Engine) Control
Request Engine Torque (TREQ)
  From specified throttle

## Slide 19: Speed Control

## Slide 20: Speed (Generator) Control
Request generator speed (NGEN)
  From specified throttle

## Slide 21
AVTC Model Based Design Curriculum Development Project

## Slide 22
HEV Supervisory Control and Fault Diagnosis
Module 3-2

## Slide 23: Thermostatic control
Lesson 2
Module 3
Engine and Generator Control

## Slide 24: Thermostatic Control
This is one of the most basic type of control
  Characterized by operation in two states: Off or On
  Classic example is a typical home AC or heating system
  For heating, when the temperature falls below a set point the heating system comes on a fixed heat deliver
  When the temperature surpasses the set point, the heat system is turned off
  There is usually a hysteresis band or delay that keeps the system from rapidly cycling
Pros:
  Very easy to code
  Easy to calibrate
Cons:
  Very constrained
  Not much room to optimize

## Slide 25: Thermostatic SOC Control for a Series HEV
For example: SOC control
Set SOC max and min limits
  Switch between an EV mode and a “recharge” mode
Single generator speed and engine torque pair
  Set point should be efficient for both motor and engine
  Must be able to achieve charge sustaining
    Must provide enough power for all driving conditions

## Slide 26: Thermostatic SOC Control for a Series HEV
Stop-Start Issues:
  Noise and Vibration (NVH)
  Emissions – Catalyst thermal
  Emissions – Catalyst cooling
  Emissions – Catalyst chemistry
  Efficiency
Upcoming Material:
  Module 3-3 shows how to use model-based optimization techniques to select an operating point for a thermostatic control
  Module 4-2 is a demo on how a thermostatic control can be built in Simulink

## Slide 27
AVTC Model Based Design Curriculum Development Project

## Slide 28
HEV Supervisory Control and Fault Diagnosis
Module 3-3

## Slide 29: optimization
Lesson 3
Module 3
Engine and Generator Control

## Slide 30: Introduction
One of the most basic (and useful) functions of model-based design is the ability to use models for optimization
  It is possible to do optimization experimentally with actual plant hardware
  This can be expensive, requires time, and is difficult to do on complex systems
An excellent example of this is the selection of operating points for a series engine-generator
  Selection of gear/belt ratio between the two devices
  Selection of best possible operating point for thermostatic control
  Selection of a optimal power path for a more sophisticated control (we will talk about this later)

## Slide 31: Demonstration