## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
Module 4
State of Charge (SOC) Regulation
HEV Supervisory Control and Fault Diagnosis

## Slide 3: Module Overview
SOC regulation is critical to designing a successful HEV
  Controlled by supervisory control
  Poor SOC regulation can lead to battery failure and poor efficiency
    Maximum and minimum SOC limits
    Charge sustaining region
A combination of PID and feed-forward control are used to control SOC

## Slide 4: Module Overview
In this module, we will do the following:
  Review SOC and its importance
  Review PID controller tuning methods
  Demonstrate PID control
  Demonstrate feed-forward control
  Demonstrate PID control with feed-forward control

## Slide 5
AVTC Model Based Design Curriculum Development Project

## Slide 6
HEV Supervisory Control and Fault Diagnosis
Module 4-1

## Slide 7: Review of Importance of SOC regulation
Lesson 1
Module 4
State of Charge (SOC) Regulation

## Slide 8: What is SOC?
Dimensionless value describe amount of usable charge in battery
  Expressed as a percent capacity/energy of total capacity/energy
  Based on open-circuit voltage (VOC)
What happens with poor SOC regulation?
  Can overcharge or undercharge the battery
  Inefficient operation

## Slide 9: Importance of SOC Regulation
Important to have control limits preventing overcharging and depleting of battery
Battery Management System (BMS) will disconnect the battery if it is in danger

## Slide 10: Supervisory SOC Regulation
For a plug-in HEV, one typically wants to utilize the largest possible SOC swing (enhanced range)
Once near the target minimum SOC, the vehicle supervisory control needs to maintain SOC within a desired range

## Slide 11: Supervisory SOC Regulation
Factors to consider when determining charge sustaining region:
  Lower charge allows for better electric range
  Battery internal resistance may be higher at low SOC which
  Pack durability – deep discharge can cause more rapid degradation of the battery
  Size of charge sustaining region
    Bigger gives more freedom to optimize – can be better for efficiency
    Smaller is more constrained – more likely to end cycle with desired SOC rather than too high or too low

## Slide 12
AVTC Model Based Design Curriculum Development Project

## Slide 13
HEV Supervisory Control and Fault Diagnosis
Module 4-2

## Slide 14: PID control
Lesson 2
Module 4
SOC Regulation

## Slide 15: What is PID Control?
Controller that acts on error signal three ways
  Proportional: Control signal is proportional to the error
  Integral: Control signal proportional to the integral of the error
  Derivative: Control signal proportional to the derivative of the error
Relatively simple control strategy that is used across industry
  If you really know how to use PID control and feedforward control you will be able to handle a broad range of control techniques
  The approach is also very consistent with the MBD approach as long as you are not doing a lot of “hand tuning”

## Slide 16: PID Controller

## Slide 17: Proportional Control
Often leads to an equilibrium with significant steady state error

## Slide 18: PI Control
Gets rid of steady state error
Can lead to oscillations

## Slide 19: PID Control
Can reduce oscillations
Difficult to implement in real life
  Unstable

## Slide 20: Selecting PID Gains
There are many ways of selecting gains
  Some are more “model-based” than others
  Most conventional ways require a linear model of the system
Some techniques are:
  Set-point weighting – calculate gains based on a formula and a first-order model of the system
  Loop Shaping – uses a Nyquist approach similar and is similar to above
  Ziegler-Nichols – Empirical technique typically done on the physical plant and some empirically derived equations
  Improved Ziegler-Nichols – improvement on above
All of these techniques and more can be found in control textbooks and online (Google “PID tuning site:.edu”)

## Slide 21: Selecting PID Gains
So what approach should one use to take advantage of “Model-Based” benefits?
  The answer is really almost any of them…
Some techniques require a linear model of the plant
  If your plant is pretty linear, you can fit a first-order or second order and solve for your PID gains
  You can also use the “empirical” Ziegler-Nichols technique on a linear model – just tune the gains in comfort of your office chair rather than on the actual plant

## Slide 22: Selecting PID Gains
For plants that are non-linear, there are a couple of options:
  Linearize the plant model around your operating point (and hope for the best…)
  Ignore that the plant model is non-linear and use an empirical technique (and hope for the best…)
The truth is that the world is full of non-linear systems and we manage to control them with PID controls all of the time
  Control text books spend a lot of time talking about linearity that is true
  This is not necessarily what a person doing applied control spends time worrying about

## Slide 23: Selecting PID Gains
One of the more effective ways to select PID gains is to let Matlab do the work for you:
  Make a Simulink model of your plant and control with P, I, and D as workspace variables
  Define a standard reference input to your control (a series of step inputs, ramp, actual commands - whatever you think is correct)
  Define some scalar error metric you want to minimize and output it to the workspace
  Wrap an optimizer around the Simulink code so that it picks the best P, I, and D values to minimize the error
This takes some time to learn how to do and doesn’t have much “finesse” – but it gets the job done
  You can also make the control algorithm complex, add feedforward control, etc. and still get an answer

## Slide 24: PID Tuning Rule Example
Ziegler-Nichols Frequency Method
  First, set P gain (KM) equal to 0 and increase until you achieve sustained oscillations
  Record oscillation period (PM)
  Calculate gains:

## Slide 25: PID Tuning Rule Example
Sustained oscillations with oscillation period PM

## Slide 26: PID Tuning Rule Example
Another Method
  Need step response of open loop system

## Slide 27: PID Tuning Rule Example
  P Control:
PI Control:
  PID Control:

## Slide 28: Nonlinear Plants
For certain types of nonlinear plants, a simple control works fine
For others, the nonlinearities are so great that they can’t be ignored
The basic PID concept can be extended for these scenarios

## Slide 29: Gain Scheduling
Gain scheduling is a technique that can effectively deal with non-linear plants (without all of the mess…)
General idea is:
  Divide up the plant operation into “zones” – these zones should be “scheduled” based on things that represent the nonlinearities
  Develop PID gains for each of the zones using any technique
  Verify that the P, I, and D gains are relatively smooth in adjacent zones
  As the plant moves from one zone to the next, swap out your P, I, and D gains accordingly
This is not a theoretically rigorous technique put is used extensively for applied control

## Slide 30: Gain Scheduling

## Slide 31: Hysteresis
Operating in zone 1
  Will not switch to zone 2 gains until engine speed reaches ωb

## Slide 32: Hysteresis
Operating in zone 2
  Won’t switch back to zone 1 gains until engine speed reaches ωa

## Slide 33: HEV Example - PI Gain Scheduling
As SOC gets well below SOC target, gains increased
  SOC increases towards target
As SOC gets higher than SOC target, gains decreased
  SOC decreases towards target

## Slide 34: Demonstration

## Slide 35
AVTC Model Based Design Curriculum Development Project

## Slide 36
HEV Supervisory Control and Fault Diagnosis
Module 4-3

## Slide 37: Pure feed-forward control
Lesson 3
Module 4
SOC Regulation

## Slide 38: Demonstration

## Slide 39
AVTC Model Based Design Curriculum Development Project

## Slide 40
HEV Supervisory Control and Fault Diagnosis
Module 4-4

## Slide 41: Pi + feed-forward control
Lesson 4
Module 4
SOC Regulation

## Slide 42: Demonstration