## Slide 1
Module 5
Fault Diagnosis
HEV Supervisory Control and Fault Diagnosis

## Slide 2: Module Overview
In this module, we will discuss some concepts related to fault diagnosis
Fault diagnosis is the process by which one monitors a system to check for undesired behavior (i.e. component faults)
This function is distinctly different the control action – but often time the discovery of a fault might require change in control action
The Fault Diagnosis process is generally broken down into three phases:
  Detecting a Fault; Isolating a Fault; and Remediating a Fault
In this module, we will discuss:
  FMEA
  FTA
  Basic techniques for fault diagnosis

## Slide 3: Fault determination
Lesson 1
Module 5-1
Fault Diagnosis

## Slide 4: Why Fault Diagnosis?
Fault Diagnosis process is generally broken down into three phases:
  Detecting a Fault: “Hey, I just noticed something is working right.”
  Isolating a Fault: “This thing right here is broken.”
  Remediating a Fault: “I just changed something so that we don’t use that broken thing.”
We do fault diagnosis to:
  Improve safety
  Improve reliability
  Ensure critical functions of the vehicle (like emissions control) are operating properly

## Slide 5: What is FMEA and FTA?
Failure Mode Effects Analysis (FMEA)
  A bottom-up approach
    How can this component fail?
    What happens when it fails?
    How likely is it to fail?
    How bad is it going to be when it fails?
    How easy can I detect that it failed? (and presumably do something about it)
Fault Tree Analysis (FTA)
  A top-down approach
    What are some high-level “bad things” that can happen?
    What kinds of failures would need to happen to cause those things?
    What kind of failures would need to happen to cause those failures?
    What kind of failures would need to happen cause the failures that cause the failure?
    You get the point…

## Slide 6: Key Differences
Fault Diagnosis – This is an algorithm that runs on an ECU
FTA/FMEA – These are off-line tools that you can use to figure out what faults you should be concerned with
All of these techniques are enhanced by model-based techniques
We will now have a demo from Amanda Hyde illustrating some key concepts for successfully doing FTA/FMEA analysis

## Slide 7
1/15
Fault Diagnosis
Purpose of fault diagnosis is to determine…
  Potential failures
  Causes and effects of potential failures
  How to prevent failures from occurring
  How to mitigate failures and their effects
Tool to assess risk
Two types:
  Fault Tree Analysis
  Failure Modes and Effects Analysis (FMEA)

## Slide 8
2/15
Fault Tree Analysis

## Slide 9
3/15
Fault Tree Analysis
OR gate: Upper level event occurs if any one of the lower level events occur
AND gate: Upper level event occurs if all of the lower level events occur
K/N gate: Upper level event occurs if K or more of the N lower level events occur

## Slide 10
4/15
Failure Modes and Effects Analysis (FMEA)

## Slide 11
5/15
FUNCTIONS Area
Enter components and their functions in this column
This should involve nouns and verbs (not just a list of components)
Functions (or functional requirements) are the utility the components/subsystems/systems provide to the vehicle and ultimately to the customer
Good
Wrong

## Slide 12
6/15
POTENTIAL FAILURE MODES Area
Enter all potential failure modes and effects of failures
Every potential failure should have its own line, there should not be a list of failures in a single ‘Failure Mode’ box
  Hint: if you typed a comma there, it’s probably incorrect
Correct

## Slide 13
7/15
POTENTIAL FAILURE MODES Area
Potential failure modes are always related to functions or requirements
This can include
  No function
  Partial function
  Intermittent function
  Unintended function
  Overachieving function
Potential Effects of failure are related to
  Other parts/Sub-components
  Assembly
  Subsystem/System
  Vehicle
  Government regulations
  Customer (Internal and End User)
Examples
(This was a sample FMEA for a marker)
Examples

## Slide 14
8/15
POTENTIAL CAUSES Area
Enter all potential causes of failure
Every potential cause should have its own line, there should not be a list of causes in a single ‘Cause of Failure’ box
  Hint: if you typed a comma there, it’s probably incorrect
Correct

## Slide 15
9/15
POTENTIAL CAUSES Area
Relationship between failure, effect, and cause
A common mistake is confusing failure modes, effects, and causes
The following technique can assist in relating cause back to failure, not effect
Technique
Example

## Slide 16
10/15
POTENTIAL CAUSES Area
Prevention Controls: Design actions planned or completed to prevent or reduce occurrence of failure, provide details and Best Practices used. Examples include:
  Reuse of proven designs
  Best practices/lessons learned/DFSS
  CAE/Analysis Simulation
  Design Checklists
  Material Guidelines/Design Standards
  Errorproofing
Examples
(This was a sample FMEA for a marker)
Detection Controls: Analytical or physical validation method planned or completed. Examples include:
  Math based validation
  Component level testing
  Subsystem level testing
  System level testing
  Durability testing

## Slide 17
11/15
Determining Severity Number

## Slide 18
12/15
Determining Occurrence Number

## Slide 19
Determining Detection Number
13/15

## Slide 20
High Voltage Battery
Example
14/15

## Slide 21
FTA
Single and Multipoint Failures
Can be more abstract with functions (early design stages)
Graphical, to the point
Top-Down (failure  cause)
FMEA
Single Point Failures
Uses well defined components (advanced design stages)
Table format, broad and comprehensive
Bottom-Up (cause  failure)
Comparison
15/15

## Slide 22: Detection Techniques
Lesson 2
Module 5-2
Fault Diagnosis

## Slide 23: Introduction
There are several different techniques for detecting faults
We will discuss the following here:
  Threshold techniques
  Residual generation
In order to determine what faults should be detected, you can use previously discussed techniques:
  FTA
  FMEA
OBD regulations also contain a great deal of legislative requirements

## Slide 24: Threshold Techniques
This is the easiest fault diagnosis to implement (and is a perfectly fine technique)
The basic idea is straightforward:
  Certain measurements/estimates/parameters should stay within certain limits, or thresholds
  If one of these values goes outside the threshold something is wrong
Some examples:
  Component temperatures
  Component speeds
  Difference between component speeds (clutch failures)

## Slide 25: Threshold Techniques
These techniques are what some might call “expert-based” – meaning you need to know the system well to be able to design them
  Much of fault diagnosis is this way – FTA/FMEA are not things that can be done well without good knowledge of the system being studied
Besides some of the obvious things, you can also look at more “exotic” signals:
  Certain control signals, the value of an integral gain, may signify that something is not right
  If you have some kind of adaptive parameter in your control, if it moves to far from nominal you might have an issue
  Various empirical methods have been used for things like catalyst OBD
These techniques may or may not be able to isolate the fault
  For example, sensing that your batteries are too hot is not enough information to determine what the cause
  This fault could result from a number of failures

## Slide 26: Threshold Techniques - MBD
Threshold techniques can be enhanced by MBD techniques
  Can help determine the threshold parameters and the detection scheme
  Can allow you to SAFELY insert faults through a SIL or HIL environment
As with any model-based techniques, your results will only be as good as your model is
The SAFETY aspect of using models though is very important
Examples for Discussion:
  Basic thresholding
  Redundant throttle signals
  Catalyst health monitoring

## Slide 27: Residual Generation
There is an entire field of fault detection that uses a technique of residual generation
Residual generation is inherently model based
  It can use “normal” I/O models
  It can use observers, which are an advanced control technique
The basic idea is the following:
  In your controller, you run a model of the plant you are controlling
  You send the same control outputs to your real plant as you do the simulated plant
  You then compare the measured response of the actual plant to the simulated response of the simulated plant
  If there is a difference then you either have a fault (or your model is not correct…)

## Slide 28: Model-Based Fault Diagnosis
Residual Generation:
a signal that should take nonzero value in the presence of one or more faults, and zero otherwise. The residual is obtained by comparing the plant output with the output of a model or several models.
Modeling error:
Any inaccuracy in the models used results in nonzero residuals, usually with amplitude strongly dependent on the system input.