## Slide 1
HEV Supervisory Control and Fault Diagnosis
Module 6

## Slide 2
Module 6:
  Overview of the Control Design Process

## Slide 3
I
II
III
Requirements to specifications…
Sub-system(s) development…
Sub-system(s) integration and final release
Automotive Model Based Control – Comprehensive Process

## Slide 4
I. Requirements to Specifications

## Slide 5
II. Sub-system(s) Development

## Slide 6
III. Sub-system(s) Integration

## Slide 7
I/O and constraints
Identify the I/O and constraints
System model (full model)
High fidelity model that is the best possible representation of the system
Control-oriented
model
Less accurate than the truth model but still a good representation of the system
Controller design
Design the control . logic with the control-oriented model
Plant model
Control model
Model Based Control

## Slide 8
Verification vs Validation
Model in Loop (MiL)
Software in Loop (SiL)
Processor in Loop (PiL)
Hardware in Loop (HiL)
Rapid Prototyping (RP)
Automotive Software V & V

## Slide 9
Verification vs Validation
Requirements
Specifications
Requirements indicate what the system is desired to do
Focus on the customer’s wants and needs (functional)
Requirements once processed lead to specifications
* End user perspective *
Specifications indicate how a system has to work to do a desired task
Focus on capturing requirements in a precise form to enable the development process (technical)
Specifications are ‘implementable’ requirements
* Developer perspective *
Validation
Verification
Ensuring that the system matches up against requirements
  Building the right thing…
Ensuring that the system matches up against specifications
Building it right…
A system that passes all verification tests can still fail in the validation phase !!

## Slide 10
Model in Loop (MiL)
Control model
Plant model
 Signals 
Virtual OS
Model in Loop- study the performance of the system and design the control algorithm(s) in a virtual environment
Inexpensive, easier to implement but effective mainly in the early phases of development
The control and plant models can be separate but
  run in the same environment
  connected directly by a virtual bus that transfers signals to & fro
Important to build models and develop test cases keeping in mind
future V&V processes right from the MiL phase.

## Slide 11
Software in Loop (SiL)
Software in Loop - verify that code generated from a model will function identically to the model
Control models created in the modeling environment are built and compiled to software code – automatic code generation tools are generally used (Simulink Coder for eg)
Software code runs in the modeling environment while the plant model remains the same as in the case of MiL.
Increased simulation speed by including compiled code in place of interpretive models
SiL enables the inclusion of control algorithm functionality for which no model exists
Control model – Software C Code
Plant model
 Signals 
Virtual OS
Modeling Environment

## Slide 12
Processor in Loop (PiL)
Plant model
 Signals 
Virtual OS
Embedded Target with direct Interface (Processor)
Direct Interface
(eg. Ethernet)
Control System
Code Generation
Control Model
Processor in Loop– an intermediate step between software in loop and hardware in loop – control system converted to code and flashed onto the embedded target
Embedded target interfaces directly with the plant model running on the modeling environment
System can be checked for errors associated with the code generation process (if any)

## Slide 13
Offline Simulation
Real-Time Simulation
Simulation over-run
need for Real-time Simulation –HiL

## Slide 14
Hardware in Loop (HiL)
Hardware in Loop – facilitates validation in real-time with actual sensor and actuator signals
The ‘hardware’ in loop - a dedicated simulator with the plant model running in real-time
HiL enables extensive testing of multiple scenarios including potentially dangerous test cases without having to actually damage real mechanical/electrical systems
Simulator capable of handling test drives outside the range of what real vehicles can do.
Tests are reproducible and automatable (lights-out testing)
Real time OS
Real time OS
Embedded Target (ECU)/RP Target
Signal Harness (Sensor & Actuator signals)
Control System
Plant Simulator
Initial setup and data logging via PC interface
I/O

## Slide 15
Hardware in Loop (HiL)
Real time OS
Plant Simulator
CPU running a RTOS
CAN interface
Analog I/O
Digital I/O
Firewire/HS interface
LAN interface
Interface with additional actual hardware/controllers
This interface is the same as what is used in an actual vehicle b/w different ECUs to communicate
This interface is used to communicate with a PC
(for data recording etc)
This is used to interface with additional RT simulators
Test ECU interface
This is how signals are sent to & from the test ECU – equivalent to a vehicle wiring harness connected to a production ECU
Real time OS
Embedded Target (ECU)/RP Target
Control System
I/O

## Slide 16
Rapid Prototyping (RP)
Rapid prototyping - enables realization of control strategies within short lead times
All control models converted to code and run real-time on a rapid prototyping simulation system connected to various analog and digital I/Os
Control is tested on the actual plant (prototype/existing vehicle with all systems working)
Real-time calibration is possible, enabling tuning of parameters with the control system running on a vehicle
Rapid prototyping is not always the final implementation of automotive software – more extensive and comprehensive testing might be required before a final release
Real time OS
Real time
Rapid Prototyping Target
Signal Harness (Sensor & Actuator signals)
Control System
Actual Plant
Initial setup and data logging via PC interface
I/O
Code Generation
Control Model

## Slide 17
Thank You!