## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
Module 2
Propulsive Torque Control
HEV Supervisory Control and Fault Diagnosis

## Slide 3: Module Overview
Control of propulsive torque is one of the key functions of a hybrid supervisory control
  A supervisory controller typically issues requests to lower level controllers to fulfil
  In a hybrid vehicle, these lower level control algorithms are things like engines, electric machine inverters, and transmission controllers
  It is not necessary for these control algorithms be running on separate microcontrollers – but there is usually some segregation
    For instance, inverters will typically be independent
    Supervisory, engine, and transmission controls may be run on a single microcontroller
This is one of the most basic and most important functions of a supervisor control

## Slide 4: Module Overview
In this module, we will do the following:
  Introduce some basic control terminology and concepts
  Compare and contrast feedback and feedforward control
  Discuss how one would practically develop a feedforward control
  Discuss a few applications of feedforward control in hybrid vehicles
  Highlight various situations where component limitations may need to be enforced for hybrid electric vehicles

## Slide 5
HEV Supervisory Control and Fault Diagnosis
Module 2-1

## Slide 6: Terminology and block diagrams
Lesson 2-1

## Slide 7: Terminology and Block Diagrams
The Plant: the System you are trying to control
For MBD you will normally have both a virtual plant (a model) as well as the physical plant
Examples:
  An entire vehicle
  A engine
  An electric motor
  A low-level actuator

## Slide 8: Terminology and Block Diagrams
Plant models can very in fidelity
  High-fidelity means more complicated
  Low-fidelity means less complicated
The appropriate fidelity is determined by your goals
These could be really, really complicated
OR
Really, really simple
Notes: Get example of Inverter model

## Slide 9: Terminology and Block Diagrams
Block diagrams are an important “language” for communicating and designing control algorithms as models
  Simulink Diagrams are built using this language – but block diagrams pre-date Simulink
A introductory controls text book will provide more details on how to construct them and interpret them

## Slide 10: Terminology and Block Diagrams
Important features:
  Desired Output of Reference (u)
  Plant Output (y)
  Measured Output (ymeas)

## Slide 11: Terminology and Block Diagrams
Error junction:
  Difference between desired output and measured output
  Usually the input into a classic feedback controller
  High error usually means higher control action and vice-versa
  Sign also matters (sometimes you might need to invert it)

## Slide 12: Terminology and Block Diagrams
The actual plant hardware is shown below
  It is important to be able to understand where the plant stops and the control begins

## Slide 13: Terminology and Block Diagrams
Software of block diagram
  We are interested in developing this area of the block diagram
  Software also has to run on something, like an embedded controller

## Slide 14: Feedback vs. Feed-forward Control
Feedback Control
  Compares plant output to desired plant output (the reference)
  This type of control can “see” when what you are getting is not what you are asking for
Feed-forward Control
  Has no “knowledge” of plant output – instead it operates on the reference (and other signals) to give a “best guess” of what the input to the plant should be
  This type of control can’t see if you have achieved your desired reference condition

## Slide 15: Feedback vs. Feed-forward Control
Feedback Control
  Pros: Reacts to things that might cause your output to behave differently than expected (i.e. disturbances)
  Cons: Can go unstable (i.e. behave erratically); can be slower to respond to reference changes than feed-forward control
Feed-forward Control
  Pros: Can react to changing references quickly
  Cons: Can’t react to disturbances; has no idea if it is actually regulating the reference input
Fortunately these are often used together
  You get the best of both and diminish the negative attributes

## Slide 16
AVTC Model Based Design Curriculum Development Project

## Slide 17
HEV Supervisory Control and Fault Diagnosis
Module 2-2

## Slide 18: Basic feed-forward control
Lesson 2-2:
Module 2
Propulsive Torque Control

## Slide 19: Feed-Forward Control

## Slide 20: When to Use Feed-Forward Control?
The easiest answer to this question is usually “whenever possible”
  If properly used, feed-forward control be help increase the performance of a control
  It allows you to take advantage of any knowledge that you have of the plant you are controlling to give quicker responses
  It typically decreases the gain of the feed-back control which improves stability
  It can allow satisfactory control of a non-linear system with a linear control
In applied control, especially automotive control, feed-forward control is invaluable and used extensively
  You will find that this topic is not dealt with extensively in most controls textbooks
  Regardless, feed-forward control is perfectly aligned with the MBD philosophy

## Slide 21: How to Develop a Feed-Forward Control
A feed-forward control for a low input/output system is usually pretty straightforward to develop – provided you have access to an accurate model or can conduct experiments on the plant
At the most fundamental level, FF control can be nothing other than the plant acting in reverse:
  Usually an input drives and output – that is normal causality
  For a FF control, you know the output that you want (the reference) and want to calculate the required plant input (the control output) to get it
If you run experiments, you can just develop a DOE and use that data to develop a steady-state “map”
If you have a model, you have at least two options:
  Invert the model (this keeps the dynamics) and can be kind of tricky
  Run a DOE on the model and extract the same kind of map as you would the actual plant

## Slide 22: Feed-Forward Control
To illustrate these concepts with a simple sample, we will explore feed-forward control of a small PMDC motor
  This is a simplified example for understanding
  We will get to more complicated examples that are hybrid vehicle specific later

## Slide 23: Speed Control of PM EM
Input to controller is the desired motor speed

## Slide 24: Speed Control of PM EM
Controller outputs a voltage to be
applied to the motor plant model

## Slide 25: Speed Control of PM EM
Input voltage from the motor produces
an actual motor speed

## Slide 26: Speed Control of PM EM
How might the controller determine voltage?
  Lookup table (Voltage vs. Speed map)
  Controller would pick a voltage based on the speed requested
  These could be determined from running the testing the motor and then assuming that the motor you are controlling behaves identically
    This is an important limitation/assumption in FF control
Vm (V) | N (RPM)
1 | 100
2 | 230
… | …
12 | 1500

## Slide 27: Speed Control of PM EM
What about different operating conditions?
  Temperature has an effect on speed of motor
    Colder = more friction
  To account for these different conditions, you might need to calibrate at these points
Vm (V) | N (RPM)
1 | 100
2 | 230
… | …
12 | 1500
T=20° C
Vm (V) | N (RPM)
1 | 80
2 | 210
… | …
12 | 1200
T=-10° C
Vm (V) | N (RPM)
1 | 110
2 | 240
… | …
12 | 1700
T=50° C

## Slide 28: Speed Control of PM EM
Another disturbance: Load Torque
  What if the PM motor is rotating something?
  This can cause load torque can vary greatly
  A FF control generally might not be aware of what the load torque is (that is why it is a disturbance…)
Also consider that even “identical” will have part-to-part variation
Aging can also change the behavior of a system
Overall, Feed-Forward Control can be of
great value even with its limitations.

## Slide 29: Feed-Forward Control in an HEV
At the component level, feed-forward control is used extensively:
  Electric Motors Inverters
  Engine Controllers
  Electric Air Conditioning Control Systems, etc.
Engines controller use it heavily:
  Fuel Maps
  Volumetric Efficiency Maps
  Spark Maps
  Fuel Enrichment Maps
  And on, and on, and on…

## Slide 30: Feed-Forward Control in an HEV
At the supervisory control level, there are also many possible examples of FF control
  In the series HEV example we discuss later, we’ll demonstrate how it can be used to help control State of Charge in an energy storage system
The example show here is for a inverter which uses current as the input
  Some inverters actually have torque as an input
  We assume that we don’t have one –BUT – we would like it to act like it is torque controlled
FF control is a great choice for this because you can reliably relate current to torque at a particular speed

## Slide 31: Hybrid Vehicle Example
Overall Vehicle block diagram

## Slide 32: Hybrid Vehicle Example
Driver determines the brake and accelerator pedal positions to demand torque
  Based on difference between desired and actual vehicle velocity

## Slide 33: Hybrid Vehicle Example
Powertrain Controller determines propulsive and brake torque based on pedal inputs

## Slide 34: Hybrid Vehicle Example
Propulsive torque request
  Software decides torque request based on pedal position- Feed-forward control
  This is usually non-linear – the shape of which is a throwback to how a gasoline engine responds to a change in throttle position

## Slide 35: Hybrid Vehicle Example
This propulsive torque control can be implemented into feed-forward control system
  Accelerator position determines torque request
  Controller outputs current to electric motor plant

## Slide 36: Hybrid Vehicle Example
Feed-Forward Control block would contain a map relating desired torque to current at various motor speeds
  Similar to previous PM EM example

## Slide 37: Hybrid Vehicle Example
Vehicles do not typically have torque sensors
    Feedback via sensors is not possible
- BUT -
The Driver is torque sensor
  Adjusts accelerator position based on the desired speed of the vehicle
  This adjusts for disturbances like wind, grade, etc.
So in this case, the driver provides the feedback loop so that the desired vehicle operation is achieved

## Slide 38
AVTC Model Based Design Curriculum Development Project

## Slide 39
HEV Supervisory Control and Fault Diagnosis
Module 2-3

## Slide 40: Component limits and saturation
Lesson 2-3
Module 2
Propulsive Torque Control

## Slide 41: Introduction
One important function of a supervisory control can ensuring that components are kept within safe operating limits
It is also important when spitting torque amongst different torque sources to account for these limits
In the series HEV case-study that we are looking at here, there are several components which will have limits:
  Engine: max speed, min speed, peak torque curve
  Motor: max speed, peaking torque curve, continuous torque curve
  Generator: max speed, peaking torque curve, continuous torque curve
  Battery: fuse limits, BMS charge/discharge limits, SOC limits

## Slide 42: Engine Limitations
Engines are typically controlled by sophisticated controls which look out for the interest of the engine
  Rev limiters keep you from over speed
  Idle speed controls try to keep you from stalling
  Max torque is limited by physical limits of the engine (breathing, etc.)
  Sophisticated diagnostics keep on eye on many other things
From a safety perspective, engines will generally look after themselves
-BUT-
You need to make sure you account for the limitations in the control design

## Slide 43: Motor/Generator Limitations
Motors and generators also typically have sophisticated controls which keep things under control from component safety perspective
  Max speed can be limited (not always!)
  Torque/Current is often not straightforward due to peaking
EMs typically have continuous and peak ratings for torque or current
  Manufacturers rate these differently, so you need to understand what the meaning of this data is
  A peak rating might be the current/torque the motor can sustain for 10 seconds before the windings get to hot
  After this period, you would need to run at a lower condition for a certain amount of time before peaking
Many EM controllers do not give you any information to help you decide how you should limit the torque
  You could play it safe and stay below the continuous rating – but the peak rating might be twice the continuous rating

## Slide 44: Battery Limits – 1/2
The battery cells in a pack are completely passive and need looked after by a Battery Management System (BMS)
  Checks temperatures of cells
  Checks for presence of ground faults
  Estimates State of Charge (SOC)
  Estimates short-term current limits
If the BMS sees something it really doesn’t like, it’s only recourse is to disconnect the battery from the vehicle
  This can be very bad for a number of reasons…
In many packs, the pack can often safely deliver more current then what the HV system is fused at
  Under these conditions you could possible blow a HV fuse because of what your supervisory control is doing (this is worse then the BMS doing it…)

## Slide 45: Battery Limits – 2/2
All of the previous issues with battery generally come down to allowable current over a period of time
  Fuse curves can pass short bursts of high current
  Batteries have similar limitations for short-term current limits
  Cell temperatures also dictate a current versus time limitation
SOC limits are limits as well
The supervisory control needs to be aware of these limits and respond to them appropriately
  This usually means limiting the current in some fashion
  Most of the above effects are I2R effects which are buffered by thermal mass and dissipated by cooling

## Slide 46: Model-Based Limits
Most techniques for taking care of these limits rely on some kind of model:
  These could be static:
    Many are just maps from known behavior of the component (max speed, torque curves, etc.)
  These could be dynamic:
    Short term battery limits are dynamic and usually are in the BMS controller
    Motor peaking could be dynamic based on a winding temperature estimator (these could also be static as well)
    Fuse limits could also be dynamic based on a thermal model of the fuse behavior (these could also be static as well)

## Slide 47: Component Limits
The way one approaches these limits is up to the control engineer
  Generally it is best to design your algorithm so that limits can be placed as far upstream as possible
  This allows the limitations to flow through the control in a more “natural” way
  It is also a good idea to impose the same limits as late as possible for redundancy

## Slide 48: Electric Motor Torque Limits
The most “natural” place to put a torque limit for a single torque source vehicle would be at the point where throttle pedal is converted to torque
This would propagate through the model in a normal fashion
To the rest of the control system, it will just appear that the driver is not asking for much torque
If you have multiple torque sources things can/should get more complicated
Drivability needs to be maintained as well